## Slide 1: A quantitative evaluation of Optical vs. SAR-based Wave Kinematic Bathymetry
An algorithm for deriving nearshore depth in the surf-zone from satellite imagery
By Marcel Rodriguez-Riccelli

## Slide 2: STEP 1: DETERMINE FOUR AREAS OF INTEREST
CONDITIONS
Publicly accessible hydrographic shallow water survey data
Swell-wave regime
  Negligible effects from currents
An extended nearshore region of depths below 100 m
Latitude
  Turbidity
Exposure to marine processes
Depositional / Erosional
Seafloor features
Reef, sandbar, canyon…
VARIATION

## Slide 3: STEP 1: DETERMINE FOUR AREAS OF INTEREST
1. NORTH SHORE OF O’AHU, HAWAII
21°40'19"N 158°03'42"W
Flat tabletop reef, lava spires
Highly energetic, erosional, especially in winter
Highly sloped
Low turbidity

## Slide 4: STEP 1: DETERMINE FOUR AREAS OF INTEREST
2. GOLDEN GATE, CALIFORNIA
37°47'35"N 122°33'19"W
Bay mouth formed by tectonic subsidence
Highly energetic, erosional, especially in winter
High turbidity

## Slide 5: STEP 1: DETERMINE FOUR AREAS OF INTEREST
3. DIAMOND SHOALS, NORTH CAROLINA
35°12'15"N 75°29'40"W
Shifting sandbars that extend 8 miles from shore
Broad continental shelf / slightly sloped relief, depositional coast, lower energy
High turbidity

## Slide 6: STEP 1: DETERMINE FOUR AREAS OF INTEREST
3. PUNTA JACINTO, PUERTO RICO
18°32'16"N 67°04'23"W
Highly sloped
Moderately energetic in winter, and subject to episodic extreme hurricane events late summer
Mona Canyon just offshore
Low turbidity

## Slide 7: STEP 2: DETERMINE VIABLE TIMES
MINIMUM CONDITIONS
To be able to perform Wave Kinematics Bathymetry to derive nearshore depth:
Mean significant wave height must be over 1m
Average of the highest one-third (33%) of waves (measured from trough to crest)
Additional information of swell should be recorded to inform evaluation:
Period
Direction
FOR EVALUATION

## Slide 8: STEP 2: LOAD DATA
A. ESTABLISH AOI CLASS
class AOI:
name: str
filename: str
lat: str
lon: str
crm_link: str
crm_local: float = "null"
crm_date: str = "null"
bbox_lat: float = 0.25
bbox_lon: float = 0.25
ehukai_lat = dms_to_decimal(degrees = 21, minutes = 40, seconds = 19, direction = "N") # 21°40'19"N
ehukai_lon = dms_to_decimal(degrees = 158, minutes = 3, seconds = 42, direction = "W") # 158°03'42"W
aoi_1 = AOI(name = "North Shore, Oahu, Hawaii",
filename = "ehukai",
lat = ehukai_lat,
lon = ehukai_lon,
bbox_lat = 0.05,
bbox_lon = 0.05,
crm_link = "https://www.ngdc.noaa.gov/thredds/dodsC/crm/cudem/crm_vol10_2023.nc")
B. INITIALIZE EACH AOI

## Slide 9: STEP 2: LOAD DATA
C. DOWNLOAD CRM FOR EACH AOI, STORE METADATA IN AOI OBJECT
for a in aoi_list:
local_nc = download_crm(a.crm_link, out_dir="data/crm")
a.crm_local = str(local_nc)
ds = xr.open_dataset(local_nc)
ts_val = ds.attrs.get("GDAL_TIFFTAG_DATETIME")
if ts_val is not None:
ts_str = str(int(ts_val))
date_time = dt.strptime(ts_str, "%Y%m%d%H%M%S")
a.crm_date = str(date_time.date())
else:
date_str = ds.GDAL.split("released")[-1].strip().replace("/", "-")
a.crm_date = date_str
for offset in iterate_offset(max_days):
d = (center_date + timedelta(days=offset)).date()
start_datetime = datetime.combine(d, time.min)
end_datetime = datetime.combine(d, time.max)
subset)dataset_id=ds_name,
variables=["VHM0"],
minimum_longitude=a.lon - a.bbox_lon,
maximum_longitude=a.lon + a.bbox_lon,
minimum_latitude=a.lat - a.bbox_lat,
maximum_latitude=a.lat + a.bbox_lat,
start_datetime=start_datetime,
end_datetime=end_datetime,
output_filename=outpath_d,
)
D. DOWNLOAD WAVE MODEL DATA FOR
SEVERAL DAYS AROUND CRM DATE

## Slide 10: STEP 2: LOAD DATA
E. COMPILE & STORE LIST OF DATES/TIMES WHEN SWH > 1M
for offset in iterate_offset(num_days):
d = (center_date + timedelta(days=offset)).date()
path = dir / f"{header}_wave_{d}.nc"
ds = xr.open_dataset(path)
swh = ds["VHM0"]
swh_avg = float(swh.mean().values)
if swh_avg > 1.0:
date_str = d.strftime("%Y-%m-%d")
dates_gt1.append(date_str)
swh_gt1.append(swh_avg)
a.swh_array = swh_gt1
a.swh_dates = dates_gt1
F. STORE PERIOD AND WAVE DIRECTION FOR THOSE DATES

## Slide 11: STEP 2: LOAD DATA
EXAMPLE - DAYS ELIGIBLE FOR WAVE KINEMATICS BATHYMETRY